## Slide 1: FYP Presentation
Enhancing sdr for satellite ground station with continuous duplex operation, doppler compensation and several modulation methods
Presented by: Hari prakash kulasekaran

## Slide 2: Introduction
Modems
  Modulation and Demodulation
  Translator between analog and digital devices
SDR
  Same functionality through a software setup
  Cost efficient and highly portable

## Slide 3: Introduction
Motivations
  CORTEX CRT are expensive: $100,000
  Reduce the dependence of multiple CORTEX CRTs
  SDRs alleviate deployment challenges posed by physical modems at overseas launch sites
  Achieve seamless modification and upgrades with SDR

## Slide 4: Introduction
Background
  Previous student work: Necessary foundation
  Extend capabilities of existing GNU Radio-based SDR
  GNU Radio: Open source SDR development tool, robust signal processing features
Core objectives
  Identify and resolve design gaps
  Middleware for integration with existing systems
  Doppler compensator and additional modulation methods deprioritised

## Slide 5: Theoretical framework
Hardware components
  ADALM-PLUTO transceiver
  Interface and work together with GNU radio
Software components
  Telecommand: Uplink of data from ground to space
  Telemetry: Downlink of data from space to ground
  In-compliance to CCSDS protocols

## Slide 6: Theoretical framework
Telecommand
  Data packeting (Ground)
    Bit randomisation, BCH encoding and header-tail tagging
  BPSK modulation at 521 kHz
  Demodulation and recovery (Space)
    Handle clock recovery
    Costas loop: Down-convert signal
    Constellation decoder: Retrieve original data

## Slide 7: Theoretical framework
Telemetry
Encoding (Space)
  Implementing error correction methods( Reed-Solomon Encoding)
  Convolutional encoding
Modulation
  BPSK modulation
Demodulation and decoding (Ground)
  Constellation soft decoder
  Viterbi and RS decoding

## Slide 8: Theoretical framework
CCSDS communication protocols for telecommand
CCSDS communication protocols for telemetry

## Slide 9: Work done
Identifying design gaps
  Unable to achieve 2-way continuous communication
  Requires manual intervention for operation
  Incomplete telecommand design
Focus areas
  Space side telemetry and telecommand
Focus areas

## Slide 10: Work done
Upgrading telemetry design
Initial challenge
  Deframer deactivates without continuous input
  Manual intervention required to repeatedly send identical message
Solution overview
  Introduced “BLK TM Frame” GNU Radio block with encapsulation logic
  Actual data + 10 dummy packets before and after
  Mimic a continuous stream

## Slide 11: Work done
Integration details
Custom python script
    Message encapsulation
    Message boundary framing
  Data convertor blocks
    Synchronize with original architecture

## Slide 12: Work done
Upgrading telecommand design of SDR
Initial challenges
  Space-side processing stopped at CLTU-level post-demodulation ( highest layer in protocol hierarchy)
  Not unpacked to extract original message
  Verification through waveform visualisation
Notes: Finishing touch

## Slide 13: Work done
Integration details
CLTU identification using start and tail sequence
Conversion to PDU format for data handling

## Slide 14: Work done
Integration details
  Mock satellite custom python codes
    Handle CLTU down-conversion
    Segmenting into 8-byte blocks
    Appending last byte from BCH codeblocks

## Slide 15: Work done
Final integration
Existing challenge
  No link between CCSDS concatenated deframer and COP execute block
  Ground station unaware of space side status
Established new link
  Telemetry transfer frames can be passed to COP execute
  Complete end-to-end communication
  Make critical decisions, operate more autonomously and efficiently

## Slide 16: Work done
Implementation of middleware
  Replicate FEP/CRT ICD functionalities
Replaced with
Foundational work
  Identifying TCP/IP port numbers for each table
  Python script for Global FEP software

## Slide 17: Testing and results
Development of test code
  Operates through TCP connection with GNU radio
  Client: Python script
  Server: GNU Radio

## Slide 18: Testing and results
Testing upgraded telecommand design
Feed 8-byte input data through vector source
Total input of 16 bytes of BCH codeblocks
8 Byte input data
7 Byte input data
1 Byte input data
6 Byte filler data
7 Byte input data
1 Byte input data
6 Byte filler data
1 byte parity
1 byte parity
Input data
Encoding
Modulation
Ground side

## Slide 19: Testing and results
Testing upgraded telecommand design
  Expected output 14 bytes after decoding
Received data
Decoding and demodulation
Newly added functions
Space side
Output data

## Slide 20: Testing and results
Testing upgraded telemetry design
  Space side: Send TM Transfer frame
  Ground side: Check if actual data was retrieved from encapsulated message
Input data
Encoding
Newly added functions
Space side
Modulation
Ground side
Received data
Decoding and demodulation
COP Execute

## Slide 21: Testing and results
Testing 2-way communication
  Configure 2 separate PLUTO devices
  Telemetry: TM transfer frame
  Telecommand: 14 byte data

## Slide 22: Conclusion and future work
Enabled simultaneous 2-way communication through functional blocks
Telecommand design
  Down-convert CLTUs to a lower level
  Alleviate dependence on waveform
Telemetry design
  Resolve deframer deactivation challenge
  Operate continuously and no manual efforts needed
  Critical information can be passed back to COP Execute block closing the loop

## Slide 23: Conclusion and future work
What has been achieved?
  More autonomous and efficient operation
  Reduced manual intervention
  Simultaneous and 2-way communication
Scope for future work
  Doppler compensator
  Completion of all ICD tables
  New modulation methods (PLOP)

## Slide 24: Learning points
Hands-on experience in space communication systems and protocols
Handling a technical project autonomously
Learning new software tools and improving python skills
Strong debugging and problem solving skills
Collaboration with industry and project supervisors
Major milestone in academic and professional growth

## Slide 25: Thank you for your attention